## Slide 1: CCAP Converged Cable Access Platform
Gerry White, Distinguished Engineer CTO Group CABU
With material shamelessly stolen from multiple industry wide CCAP Sources
July 2014

## Slide 2: Agenda
Why CCAP?
What is CCAP?
Differences to current CMTS
CCAP components & implementation
Distributed CCAP / Remote PHY
NFV & Virtualized CCAP

## Slide 3: Why do we need CCAP?

## Slide 4
More Personal
More Interactive
Pressure to reduce rack space and power
Cable Operator Challenges to Meet the Traffic Growth
More Video
More Devices
Migrate to an all-IP network with the existing infrastructure
Keep up with unprecedented bandwidth growth

## Slide 5: So What Exactly is CCAP?

## Slide 6
CCAP Objectives
Converged multi-service platform - single port per SG
Increased DOCSIS capacity / SG
Reduced cost-per-downstream
Reduce rack space per system
Scaleable deployment options

## Slide 7
Current Head End
Router
CMTS
UEQAM
analog
OOB
broadcast
narrowcast
Rcvr
Laser
OOB
combining
Separate CMTSs & EQAMs
Limited channel capacity per platform
Multiple platforms for each
Complex combining
Scaling problems as add SGs

## Slide 8
CCAP Head End
Router
CCAP
analog
OOB
Rcvr
Laser
OOB
Digital Video and data
combining
Combine CMTS & EQAM
Higher performance
Single port per SG
Simpler combining
Easier scaling

## Slide 9
CCAP with Analog Optical Interfaces
Router
CCAP
analog
OOB
OOB
Digital Video and data
Analog optics
Include optics and combining
Further space reductions

## Slide 10: CCAP
Integration of services
One port per SG
High capacity & density
Lower costs
Efficiency & scale
Centralization of resources
Hub in box

## Slide 11: DOCSIS 3.1
Goals
  Achieve 10+ Gbps in the DS.
  Achieve 1+ Gbps in the US
  Backward compatibility story with DOCSIS 3.0, 2.0, & 1.1.
  Better spectral efficiency.
Technology
  OFDM, OFDMA, LDPC
  New DS and US spectrum
  Re-use of D3.0 MAC concepts
This will allow D3.1 to offer services competitive with FTTH.

## Slide 12
CCAP Objectives
Converged multi-service platform - single port per SG
Increased DOCSIS capacity / SG
Reduced cost-per-downstream
Reduce rack space per system
Scaleable deployment options
+ DOCSIS 3.1
Chart: 
| 2000.0 | 2005.0 | 2010.0 | 2015.0
Series 2 | 2.8
Exabytes per month
Year

## Slide 13: Today’s Headend
VoD EQAM
Broadcast EQAM
DOCSIS EQAM
DOCSIS Combining Network
VoD Combining Network
Bcast Combining Network
Forward Combiner
Forward Combiner
HFC
HFC
SG 1
SG N
Data
VoIP
IP Video
Linear
VoD
NPVR
IP Services
Digital Video Services
CMTS
SDV EQAM
SDV Combining Network
Inefficient EQAM capacity utilization, complex combining networks

## Slide 14: Integrated CCAP Architecture
Forward Combiner
Forward Combiner
HFC /PON
HFC /PON
SG 1
SG N
Data
VoIP
IP Video
Linear
VoD
NPVR
IP Services
Digital Video Services
Integrated CCAP
CMTS
Universal EQAM
Increase capacity & reduce cost, rack space and power consumption
One port per SG

## Slide 15: What goes into a CCAP?

## Slide 16: Generic CCAP Components
Supervisor & packet engine
DOCSIS line cards
DOCSIS line cards
Active line cards
Spare line card(s)
BH PIC
RF PIC
Digital and RF mid-planes
DOCSIS + EQAM
Timing
Northbound interfaces
To core
10G Ethernet
Southbound interfaces
To HFC
RF or optical
External timing
Routing
Packet engines
Control & management

## Slide 17: CCAP Front
RF Line Cards
Port per SG
Full spectrum per port
DS + US on one card or
DS cards + US cards
N+1 redundancy with integrated RF Switch
Supervisor Cards
Integrated backhaul capacity
1+1 redundancy
N * 10G interfaces
Power Supplies
5 -> 10KW

## Slide 18: CCAP – Rear
RF Line Card PICs
High density connectors
Integrated analog optics
Remote PHY digital optics
Cooling
Exhaust fans
Power Connections
Supervisor PICs
N x 10 GE ports
Management
Timing

## Slide 19: CCAP Impact
DOCSIS 3.0 + 3.1
Scale from 1 to 10 Gbps downstream per SG
100 to 200Gbps backhaul initially – more later
DOCSIS
IP and MPEG video
narrowcast and broadcast
Next generation silicon – processing, packet forwarding, DOCSIS
High level of integration
Reduced cost per channel
Integration
Reduced combining
Integrated optics
Capacity
Convergence
Reduced costs
Reduced space & power

## Slide 20: CCAP & Remote Phy

## Slide 21
Remote Phy Goals
Remove RF from head end / hub
Replace analog fiber from hub to node with digital
Leverage Ethernet / PON and digital optics
Extend IP networking to the node
Simplify operations
Keep the node as simple as possible
Keep the complex s/w central

## Slide 22: CCAP with Centralized PHY
In a I-CCAP, the CMTS and EQAM share a common PHY
PHY provides digital to analog conversion
Clock is local to the CCAP platform
DOCSIS
L2
MAC
Common
L1
PHY
Video
L2
MAC
clock
RF

## Slide 23: CCAP with Remote PHY
DOCSIS
L2
MAC
Remote
PHY
Video
L2
MAC
clock
DEPI
UEPI
Remote PHY
Common
L1
PHY
clock
RF
Ethernet
Ethernet
The CCAP PHY chip is remotely located and connected over Ethernet
Digital to analog occurs in the Remote PHY node
Remote DTI manages transfer of time and frequency
R-DTI

## Slide 24: Fiber Deeper & Remote PHY
CCAP Core
L2 and above
DOCSIS
CM
CCAP Remote PHY
Remote PHY Signaling
Adapts CCAP to an HFC plant that contains digital fiber instead of linear fiber
DOCSIS signaling remains end-to-end
Coax
Digital Fiber (IP)
DOCSIS
PacketCable
DOCSIS
Policy Server
DOCSIS
Provisioning
DOCSIS Signaling
Internet

## Slide 25
Remote Phy Impact
Remove RF from head end / hub
Replace analog fiber from hub to node with digital
Leverage Ethernet / PON and digital optics
Extend IP networking to the node
Enabler for virtualization
Router
CCAP
OOB
OOB
Digital Video and data
Digital Optics

## Slide 26: Network Function Virtualization & Virtual CCAP

## Slide 27: NFV
NAT
VM
Firewall
VM
SBC
VM
dDOS
VM
Virus Scan
VM
IPS
VM
DPI
VM
CGN
VM
Portal
VM
PCRF
VM
DNS
VM
DHCP
VM
BRAS
VM
SDN Ctrl.
VM
RaaS
VM
WLC
VM
WAAS
VM
CDN
VM
Caching
VM
NMS
VM
Concept
  Leverage data centre tools and technology
  Run network functions in VMs in data centers
Enablers
  Hypervisor and cloud computing technology
  Improving x86 h/w performance
Value Proposition
  Shorter innovation cycle
  Improved service agility
  Reduction in CAPEX and OPEX
Applications
  CCAP?

## Slide 28: vCCAP?
With Remote PHY
  CCAP -> CCAP core + Remote PHY
With no RF interfaces CCAP core is a canditate for virtualization
  vCCAP runs in VM on standard server platform with Ethernet interfaces
CCAP = CMTS +EQAM
  vCCAP is actually vCMTS + vEQAM
  CCAP becomes vCMTS + vEQAM + R-PHY
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM
CCAP
VM

## Slide 29: Why NFV?
NFV is a direction that Service Providers are headed in an effort to reduce OPEX
It allows a generic hardware complex with specialized software applications.
It trades off specialized hardware for less optimized common platforms
It uses standard management and orchestration tools
NFV and Orchestration required is not simple but
  It is heavily leveraged from the data center
  It is mainstream technology
  It could have significant advantages especially for scaling & OPEX
Physical versus virtual will be a choice

## Slide 30: Evolved Network Infrastructure
High SLA Commercial
Select Residential
Installed Base
+ CCAP
Orchestration
Deep Fiber
Digital Fiber
Small Hub
Linear Fiber
RPHY
SHELF
NFV
Products
Applications & End to End Connectivity
FTTx OLT
ONT
Applications
Residential & Business Services Applications
RPHY
NODE
- Classic HFC
HFC
Plant
Ethernet
NID
Evolved Services Platform
CCAP-Core

## Slide 31
Gerry White
gerrwhit@cisco.com